MAISEMORE APIARIES

EXTRACTOR MOTOR

# Instructions for Use

1.	Before connecting the motor to the electricity supply, set the switch in the end plate to the middle (OFF) position and move the speed control lever to the minimum (extreme left) position.

- For maximum safety it is advisable to connect the motor to the mains through an RCD breaker.

- After switching on the mains supply move the motor end plate switch to eith the “up” or “down” position (according to the direction of rotation required), then bring the motor up to the required speed by rotating the speed control lever slowly in a clockwise direction.

- DO NOT REVERSE THE DIRECTION OF ROTATION WHEN THE MOTOR IS OPERATING AT HIGH SPEED AS THIS COULD DAMAGE THE ELECTRONIC SPEED CONTROL SYSTEM.  Always bring the motor to rest before changing the direction of rotation.

- Do not use the speed control lever as an ON/OFF switch! Switch off the motor completely before changing frames or leaving your extractor unattended.

  - Please seek our advice if you are experiencing any difficulty converting your extractor from manual to motorised.  The motor is not guaranteed against damage caused by its being connected to an extractor in an unsuitable manner.  You are advised to use one of our “motorising kits” unless you have considerable mechanical expertise.

Ideally the drive collar should rotate within a nylon bush fitted in the centre of the extractor top bar.  If you retain your own top bar the centre hole will have to be machined out accuratrely to 26mm (not a DIY job!)

IMPORTANT!.  THIS CONVERSION KIT IS NOT SUIATBLE FOR EXTRACTORS IN WHICH THE CAGE IS SUSPENDED FROM ABOVE

(eg Thorne’s Universal Lightweight).  Your cage shaft MUST be supported from underneath and should preferably rest on a ball bearing.